| TDC 150 Low-Cost-Thermometer |
| --- |
|  | Technical Data Measuring range -50 to +150°C Resolution 0,1°C in range -20 to +150°C Accuracy ±1°C in range -30 to +150°C Sensor NTC Needle type probe Stainless steel, Ø3,5 mm, L=125 mm, pointed Thermal response time (t99) 10 s (water) Operating temperture 0 to +50°C Storage temperture -10 to +60°C Display LCD-7 mm Battery 1,5 V, LR44, G13 Battery life approx. 5000 h Dimensions 24 x 26 x 85 mm Housing material ABS Weight approx. 36 g Protection class IP 65 Product-No 1340-1611 |
| Attributes |
| Fixed probe, pointed Robust and impact resistant Battery exchangeable °C/°F switchable Needle guard |